## Slide 1: Patient Health Tracking System
SAGAR K
COURSE : EMBEDDED SYSTEMS AND IOT
MENTOR : MEHAK MAJEED
SURE ProEd

## Slide 2: Contents
Introduction
Objectives
Components
General Block Diagram
Methodology
Protocols
Working Hardware Setup
Limitations of the Patient Health Monitoring Prototype
Application
Future Scope

## Slide 3
Central Processor
ESP32 S3
Communication
/Connectivity
Output the Data
Threshold Checking / Emergency Detection
Data Processing
Input From the Sensors
01
02
03
04
05
Introduction

## Slide 4
Objectives
Design and implement a portable system to measure heart rate and SpO₂.
Integrate an accelerometer for automatic detection of falls.
Implement emergency communication via GSM (SMS + Call).
Attach location information using GPS coordinates and Google Maps link in SMS.
Display vitals and alerts on an OLED display in real time.
Ensure low power consumption by updating display only when vital changes occur.

## Slide 5: Components
Seeed XIAO ESP32S3 Sense
LIS3DH Accelerometer
NEO-6M GPS (Global Positioning System) Module
(Organic Light Emitting Diode) OLED DISPLAY
MAX30102 Heart-Rate and SpO₂ Sensor
SIM800C GSM (Global System for Mobile Communication) Module

## Slide 6
ESP 32
MICROCONTROLLER
HEART RATE
SPO2
MAX30102 SENSOR
LOCATION
NEO-6M GPS Module
REAL TIME LOCATION
NEO-6M GPS Module
Accelerometer
SMS
GSM Module
Accelerometer
ACCELEROMETER SENSOR
LIS3DH Accelerometer
OLED display
General Block Diagram

## Slide 7
Methodology of Two-Wire I2C Sensor Communication
Figure: Connections between ESP32-S3, MAX30102, and LIS3DH sensors.

## Slide 8
SYSTEM POWER-UP
MICROCONTROLLER INITIALIZATION
MAX30102 SENSOR INITIALIZATION AND CONFIGURATION
SENSOR WARM-UP AND CALIBRATION
POLL MAX30102 FOR NEW DATA (WIREMAX)
START CONTINUOUS DATA ACQUISITION LOOP
DISPLAY OR TRANSMIT DATA
DATA PROCESSING AND ANALYSIS
LIS3DH SENSOR INITIALIZATION AND CONFIGURATION
ESP32S3 powers up, starts internal system clock.
Initialize two different I2C interfaces to allow simultaneous communication with two sensors.
Initialize MAX30102 sensor via WireMAX; verify sensor presence and configure parameters
Initialize LIS3DH sensor via WireACC; verify sensor presence and set accelerometer range.
Perform sensor warm-up period to stabilize readings.
Enter main while-loop to continuously acquire sensor data.
Read accelerometer data from LIS3DH via WireACC.
Process or buffer accelerometer readings as needed.
Apply algorithms to interpret MAX30102 readings to calculate metrics like heart rate or SpO2.
Update user display, or log data for monitoring.
Methodology of Two-Wire I2C Sensor Communication

## Slide 9
Methodology of I²C Bit-Banging (OLED Display)
Figure: ESp32 S3 and Oled Display connection

## Slide 10
CONFIGURE PINS
GENERATE START CONDITION
IMPLEMENT TIMING DELAY
ACKNOWLEDGMENT, STOP & SEND COMMANDS
WRITE CONTENT/UPDATE DISPLAY
SEND BYTE DATA BIT-BY-BIT
Define two GPIO pins: one for SDA (data line), one for SCL (clock line).
1
While SCL is HIGH, pull SDA from HIGH to LOW to begin communication.
3
This controls the speed of the bit-bang signals.
2
Send initialization commands over bit-banged I²C
5
Use the bit-bang send process to write data bytes corresponding to pixels
6
For each bit (starting with most significant bit), set SDA HIGH or LOW.
4
I²C Bit-Banging (OLED Display)
Methodology of I²C Bit-Banging (OLED Display)

## Slide 11
Methodology Of GPS Module Communication
Figure: ESp32 S3 and GPS Module connection

## Slide 12
GPS MODULE COMMUNICATION
Hardware Connection
Loop Continuation
UART Initialization
Using GPS Data
Receiving Raw GPS Data
Check for Valid GPS Fix
  Connect the GPS module’s TX pin to the ESP32’s RX pin (GPIO44).
  Connect the GPS module’s RX pin to the ESP32’s TX pin (GPIO43).
  print GPS information (coordinates, time, satellites) to the serial monitor for debugging.
  Repeat reading from UART, parsing, and monitoring continuously in the main loop.
Initialize UART2 at 9600 baud (standard GPS baud rate), 8 data bits, no parity, 1 stop bit.
  The system uses this GPS data to create location-tagged messages in case of emergency.
  Latitude, longitude, date, time (converted to IST) are formatted into SMS messages.
Continuously read incoming ASCII bytes from UART2, which represent NMEA sentences output by the GPS module.
  Verify if the parsed latitude and longitude data are valid (i.e., the GPS module has a fix).
  If valid, these coordinates can be used or transmitted further.
Extracting Meaningful Information
Once a complete and valid sentence is parsed,
Methodology Of GPS Module Communication

## Slide 13
Making Emergency Call
Continuous Monitoring
System Initialization
Sending SMS Alert
Triggering Emergency Alert
Post-Alert Handling
Methodology Of GSM Module Communication

## Slide 14: Protocols
Neo 6M GPS Module
Oled Display
MAX30102
(Heart rate & SPO2 )
Tower
LIS3DH Sensor
GSM Module
Satellite
NMEA (National Marine Electronics Association) protocol
I²C ( Bit-banged )
I²C Protocol
I²C Protocol
UART Protocol
AT Commands
UART Protocol

## Slide 15: Working Harware Setup
Figure: Working Model of Patient Health Tracking System
Oled Display
GPS Module
MAX30102 sensor
GSM Module
ESP32S3
ACCELERATOR Module

## Slide 16
Limitations of the Patient Health Monitoring Prototype
Sensor Accuracy
Motion artifacts or improper contact affect MAX30105/LIS3DH,
requiring calibration for reliable data.
Fall Detection
Simple acceleration thresholds risk false positives (sudden movement)
or false negatives (slow falls).
Power Consumption
Continuous operation (sensors, OLED, GPS, SIM800C) drains battery
quickly, limiting device uptime.
GPS Availability
Indoor or dense areas degrade GPS signals, impacting emergency
location reliability and alert delivery.
Cellular Dependence
No signal means no SIM800C alerts, directly impacting timely
emergency communication.
Limited User Interface
Small OLED restricts interaction and feedback,
creating accessibility issues for some users.
Contact Flexibility
Hardcoded contacts lack dynamic management. No wireless fallback impacts
communication in outages.
Scalability
Hardware and code complexity can hinder adding features
leading to performance bottlenecks.

## Slide 17: Application

## Slide 18: Future Scope
Advancements in Sensor Technology
AI-Based Predictive Health Alerts
Enhanced Connectivity
User Experience Enhancements
Integration with Healthcare Systems
Extended Applications